## Slide 1: ENGI 301 Hifi Music Player Proposal
19 Feb 2024
Nithit Bunchatheravate (Ai)

## Slide 2: Background Information
In a world where music has become a part of everyone’s lifestyle from using airpods with iPhones to custom in-ear monitors with the Sony Walkmans, each individual finetunes their music to their own taste. As an audiophile, the ability to adjust every single aspect of your listening experience is what turns a good music session to a great one. This can be accomplished in one of two ways: tuning the listening devices or utilizing an equalizer (EQ) within the music player. Being able to customize and tune your EQ is a feature missing on most devices (excluding high-end models) and you would have to rely on the streaming service EQ functions. As such, this project aims to implement a detailed EQ with lossless audio files to provide the user with the best listening experience.
Notes: Other aspects to consider
- Adding effects (as an alternative to quality)  reverb, rock,

## Slide 3: Existing Projects
Music player for USB-Speaker (No DAC)
  https://www.hackster.io/432580/usb-music-player-with-the-pocketbeagle-0b1624
Music player with DAC
  https://www.hackster.io/logan-baldridge/spotify-pod-streaming-music-to-the-pocketbeagle-57a180

## Slide 4: Improvements
Hardware
  Two customizable buttons
    Possible programming options include EQ profiles, brightness, shuffle/loop/single loop  gives the user more control and personality into their device so that the listening experience is enhanced
Software
  Personalized equalizer system built into the device (much more specific)  user can finetune their audio to their own liking for different music genres and switch between them using the customizable buttons

## Slide 5
Pocket Beagle
USB Port (USB1)
PowerBoost 1000c
Battery
SPI Screen
D/C (P1.4)
CS (P1.6)
CLK (P1.8)
MISO (P1.10)
MOSI (P1.12)
on/off
volume up
volume down
play/pause/skip/replay
custom 1
custom 2
GPIO (P2.1)
GPIO (P2.2)
GPIO (P2.4)
GPIO (P2.6)
GPIO (P2.8)
GPIO (P2.10)
Note: Bela mini is soldered onto the pocketbeagle
USB Hub
(<900 mA)
USB with downloaded music
Bela mini

## Slide 6
Pocket Beagle
3.3 V BAT Vin (P2.14)
GND (P2.15)
PowerBoost 1000c
Battery
SPI Screen
(<150 mA)
3.3 V (P1.14)
on/off
volume up
volume down
play/pause/skip/replay
custom 1
custom 2
3.3 V GPIO (P2.1)
3.3 V GPIO (P2.2)
3.3 V GPIO (P2.4)
3.3 V GPIO (P2.6)
3.3 V GPIO (P2.8)
3.3 V GPIO (P2.10)
GND (P1.16)
Note: Bela mini is soldered onto the pocketbeagle
USB Hub
(<900 mA)
USB Port (USB1)
5 V
<6 mA
USB with downloaded music
5 V
350 mA
5 V
Bela mini

## Slide 7: Components / Budget
Component | ENGI301 to Buy? | Cost
SPI Screen | Yes | 29.95
USB Hub (only need 1 port) | No | 19.99
Bela Mini | No | 89.00
PowerBoost 1000c | No | 19.95
Total |  | 167.88

## Slide 8: Helpful Links
https://www.pimusicbox.com/
https://www.beagleboard.org/projects/volumio  music control
https://learn.bela.io/products/bela-boards/bela-mini/#:~:text=On%20your%20Bela%20Mini%20cape,slot%20aligned%20on%20the%20other.  attaching bela to pocketbeagle

## Slide 9: Component Selection (Remove slide for submission)
All components must be from either: Amazon, Adafruit, Sparkfun, Digi-Key, or Mouser
Select no more than two (2) components that are not on approved component spreadsheet
  See Canvas  Files  assignments  ENGI301_project_01_parts_list.xlsx
  If there is a cheaper part that you would like to use, we can discuss in the project meeting
All components needed for the project should be listed on Slide 5
All components should have links to the website where they can be purchased
  Please trim URLs for links to Amazon
ENGI301 will supplement $25 to $35 dollars for components
  Please indicate what components need to be purchased by ENGI301
If you have a special request, we can discuss in the project meeting